Atlas  Copco  Surface drill rigs

ROC F9

Technical specification

ROC  F9

Full flexibility for large  scale production

• Combined  high strenght,  productivity and hole quality  thanks to outstanding drill system efficency

• Trouble free high productivity operation

• Single pass possibilities for increased production

ROC F9 is intended for construction sites,  quarries for construction and selective mining. The main  components are:

• Crawler type two speed undercarriage with track oscillation system

• Caterpillar turbo charged diesel engine CAT C9

• Stepless fuel saving RPM regulation system

• Atlas Copco screw type compressor

• Hydraulic cooling system for 50o C ambient temperature

• Combined warning sound and warning light

• Single section boom or folding boom system

• Hydraulic chain feed system with hose guide

• Hydraulic rock drill COP 2560

• Rock drill lubrication system

• Reduced impact pressure mechanism

• Anti-jamming system

• Automatic feed force control

• Manometer panel for setting of pump circuits

• Toe-hole drilling system

• Carousel type tube handling system

• Hydraulic double drill steel support with movable dust collector hood

• Dust collection system

| Hole range |  |
| --- | --- |
| Recommended hole range |  |
| ROC F9 | T45, T51 | 89-127 mm | 3 ½”- 5” |  |
| Hydraulic rod adding system for max hole depth, with 4,3 m (14’) extension rods |  |
| ROC F9 Single-section boom | T45, T51 | 33 m | 108’ |  |
| Hydraulic rod handling system for max hole depth, with 3,6 m (12’ ) extension rods |  |
| ROC F9 Folding boom | T45, T51 | 28 m | 92’ |  |

Specifications

Engine	Compressor

Caterpillar turbo charged, diesel engine, CAT C9, Tier III/stage 3

• Power rating at 2000 rpm ................... 224 kW	300 HP

Feed

Hydraulic chain feed with hose guide and double drill steel sup- port with movable lower guide/dust hood

• Feed extension .................................... 1 150 mm   3’9’’

• Feed rate, max .................................... 0.92 m/s	180 ft/min

• Feed force, max .................................. 20 kN	4 500 lbf

• Tractive pull, max ............................... 30 kN	6 750 lbf

ROC F9 Single-section Boom

• Total length ......................................... 8 360 mm   27’5’’

• Travel length .......................................5 110 mm	16’9’’ ROC F9 Folding Boom

• Total length ......................................... 7 700 mm   25’3’’

• Travel length ....................................... 4 610 mm   15’2’’

Atlas Copco M-01, screw type compressor

• Working pressure, max ....................... 12 bar	175 psi

• FAD, at normal working pressure....... 213 l/s	450 cfm

Hydraulic system

Hydraulic oil cooler

• Max ambient temperature ................... 50°C	122°F Pumps

• Axial piston pump (1) .........................190 l/min  50 US gal/min

• Gear pump (2) ....................................72 l/min	19 US gal/min

• Gear pump (3) ....................................38 l/min	10 US gal/min

• Gear pump (4) ....................................34 l/min	8.9 US gal/min

• Gear pump (5) ....................................33 l/min	8.6 US gal/min

• Gear pump (6).....................................33 l/min	8.6 US gal/min

Return and drainage filters (2 x 3 filters)

• Filtration rate ......................................16 µm absolute

Dust collector DCT 150 F

• Filter area ............................................15 m2 	164 sq.ft

• Number of filter elements ...................15 pcs

• Suction capacity at 500 mm wg..........350 l/s	741 cfm

• Suction hose diam...............................127 mm	5’’

• Cleaning air pressure, max .................8 bar	116 psi

• Cleaning air consumption ...................2-4 l/pulse   4-8 cfm

Safety cabin

• ROPS and FOPS approved with rubber vibration dampers

• 2 x wipers with washer

• Clear laminated glass (front and roof windows)

• Clear toughened glass (side and rear windows)

• Fully adjustable operator’s seat

• Adjustable foot rest

• Cabin light

• Rig inclination indicator

• Rear view mirror

• Fire extinguisher, 6 kg (13 lbs) dry chemical type ABE class

III type

• Outlet socket, 24 V

• Prepared with speakers for CD-radio

• Combined front mounted platform/tool box

• Electric combined engine, hole inclination and hole depth instrument

Electrical system

• Voltage ................................................ 24 V

• Batteries .............................................. 2 x 12 V, 185 Ah

• Alternator ............................................ 28 V, 95 Ah

• Work lights, front................................ 4 x 70 W

• Work lights, rear ................................. 2 x 70 W

• Work lights, feed................................. 2 x 70 W

• Warning lamp and reverse buzzer

Volumes

• Hydraulic oil tank ............................... 300 l	80    US gal

• Hydraulic system, total ....................... 380 l	100  US gal

• Compressor oil.................................... 40 l	10.6 US gal

• Diesel engine oil ................................. 32 l	8.5   US gal

• Diesel engine, cooling water .............. 60 l	16    US gal

• Diesel engine, fuel tank ...................... 400 l	106  US gal

• Traction gear ....................................... 3 l	0.8   US gal

• Lubrication tank (ECL) ...................... 5 l	1.3   US gal

Air conditioner

• Refrigerant ..........................................R134a

• Cooling capacity .................................5,5 kW

• Fan suction capacity ...........................125 l/s	265 cfm

| Hydraulic rock drill |  |
| --- | --- |
| Rock drill | Drill rig | Impact power | Hydraulic pressure, max | Impact rate | Torque, max | Weight approx |  |
| COP 2560 | ROC F9 | 25 kW | 33.5 HP | 230 bar | 3 335 psi | 44 Hz | 1 810 Nm | 1 335 lbf/ft | 187 kg | 412 lb |  |
| COP 2560EX |  |  |  |  |  |  |  |  | 249 kg | 549 Ib |  |

Transport dimensions

Hight and length

Feed dumped 1

Feed dumped 1

ROC F9 Single-section boom   Height (H1)	3 800 mm  12’ 6’’ ROC F9 Single-section boom   Length (L1)  12 300 mm  40’ 4’’ ROC F9 Folding boom 	Height (H1)	3 500 mm  11’ 6’’ ROC F9 Folding boom 	Length (L1)  11 300 mm 	37’ Feed dumped 2

ROC F9 Single-section boom   Height (H2)    3 200 mm  10’ 6’’ ROC F9 Single-section boom   Length (L2)  12 300 mm  40’ 4’’ ROC F9 Folding boom              Height (H2)    3 200 mm  10’ 6’’

ROC F9 Folding boom 	Length (L2)  13 000 mm   42’8’’

Feed dumped 2

H1

L1

H2

L2

Dimensions and weight

| Feed Height (H) |  |
| --- | --- |
| ROC F9 Single-section boom | 8 360 mm | 27’ 5’’ |  |
| ROC F9 Folding boom | 7 700 mm | 25’ 3’’ |  |

| Weight |  |
| --- | --- |
| Standard unit excluding all options and drill steel |  |
| ROC F9 Single-section boom | 16 400 kg | 36 150 lb |  |
| ROC F9 Folding boom | 16 600 kg | 36 600 lb |  |

H

3030

2500

3600

4970

330

Selection of optional equipment

Carrier

• Track chains with triple grouser pads

• Hydraulic support leg

• Hydraulic winch including wire with towing eye and wire guide, remote controlled

• Heavy duty air intake filters for engine/compressor

• Electric refuelling pump

• Diesel engine pre heater

• Insulated compressor regulation system

• Xenon work lights, 2 pcs on top of cab pointing forward and 2 pcs on top of canopy pointing to the rear

• ProCom satellite based drill rig monitoring system (only in com- bination with a written service agreement)

Safety cabin

• Clear laminated glass (front window and roof)

• Tinted toughened glass (side window and rear)

• Sun shade kit (rear side windows and rear window)

• Wiper for right hand side window

• Cab heating

• Electric heated operator’s seat

• Radio/CD

Feed

• TAC guide tube guides for drill steel support

- TAC 76 for 76 mm guide tube

- TAC 89 for 89 mm guide tube

• Feed foot extension

Hole measuring systems

• Laser receiver upgrading kit

• GPS compass aiming device

Lube oil, lube system and water mist system

• Central lubrication system, type

Lincoln

• Thread greasing device, ECG (with oil)

• Thread greasing device, brushes

(with grease)

• Artic hydraulic oil, VG 32

• Tropical hydraulic oil, VG 68

• Biological hydraulic oil, VG 46

• Water mist system with a 225 l pressurized water tank

Delivered equipment, not mounted

• Gas charging equipment for rock drill

• First 50 hours service kit for compressor

• Conversion kit for T45 drill steel

• Conversion kit for T51 drill steel

Coverage areas

25º

2350

3170

25º

1090

Horizontal reach (mm) with Single-section boom	2560

Vertical reach (mm) with single-section boom

25°

25°

2610

2440

4815

Horizontal reach (mm) with foldning boom

3490

Vertical reach (mm) with folding boom

9851 2454 01c

Printed in Sweden 2010-07

© Copyright 2010, Atlas Copco Rock Drills AB, Örebro, Sweden. All product names in this publication  are trademarks of Atlas Copco. Any unauthorised  use or copying of the contents or any part thereof is prohibited. This applies in particular to trademarks, model denominations, part numbers and drawings. lllustrations  and photos in this brochure may show equipment with optional extras. Specifications and equipment subject to change without notice. Consult your Atlas Copco Customer Center for specific information.

Feed swing angles

33°

95°

With single-section boom and folding boom

- toe-hole drilling kit (standard)