Atlas Copco Surface Drill Rigs

FlexiROC  T35  R and T40  R

Technical specification

The Radio Remote Controlled  rigs FlexiROC T35 Rand  T40 Rare the ideal choice for construction sites and aggregate quarries.

Main components:

•	Track frames with  single grouser pads and cleaning holes, hydraulic track oscillation  and two  speed traction

•	Caterpillar turbo charged diesel engine C 7 (Tier 3) or C 7.1 (Tier 4)

•	Atlas Copco screw type compressor

•	Radio Remote Control system

•	Folding boom system

•	Aluminum profile feed beam

•	Hydraulic cylinder feed system

•	Carousel type rod handling system

•	Hydraulic rock drill

| ------------------ ----------- Hole range - - - - ------- --- -- --_I |
| --- |
| Recommended hole range |
| FlexiROC T35 R | T38, T45, T51 | 64-115 mm | 2 Y2'-4 Y2' |
| FlexiROC T40 R | T45, T51 | 76-115 mm | 3"- 4 Yz" |
| Hydraulic rod handling system for max hole depth with 3.6 m (12' ) extension rods |
| FlexiROC T35 R | T38, T45/T51 | 28m/ 21m | 92'/ 69' |
| FlexiROC T40 R | T45, T51 | 28m | 92' |

•	Dust collection system

-

Specifications

FlexiROC T35 Rand T40 R

Engine

Caterpillar turbo charged, diesel, CAT C7, Tier 3/stage IliA

• Power rating at 2200 rpm ...................168 kW 	225 hp

Caterpillar turbo charged, diesel, CAT C7.1, Tier 4/stage IIIB

• Power rating at 2200 rpm ................... 168 kW 	225 hp

Feed

Hydraulic cylinder feed with hose guide and double drill steel support with movable lower guide/dust hood

•Totallength .........................................  7140mm 23'5"

• Travel length ....................................... 4 240 mm    14'

• Feed extension ...... .......................... .... I 400 mm   4'7''

Compressor

Atlas Copco OIS K-27-C l06 GD screw compressor

FlexiROC T35 R

• Working pressure, max ....................... I 0.5 bar

• FAD at normal working pressure........ 127 lis

FlexiROC T40 R

• Working pressure, max ....................... I 0.5 bar

• FAD at normal working pressure........ 136 1/s

Hydraulic system

• Anti-jamming

• Automatic feed force control RPC-F

152 psi

270 cfm

152 psi

288 cfm

• Feed rate, max .......... ........................ 0.92 m/s

• Feed force, max .................................. 20 kN

• Tractive pull, max .............................. 20 kN

Dust collector OCT 1100

184ft/min

4 400 lbf

4 400 lbf

• Damper pressure control- impact DPC-T Hydraulic oil cooler

• Max ambient temperature.................. 50°C 	l22°F Return and drainage filters

• Filtration rate........... 	...................16 fim absolute

• Fi l ter area ..................... .......................!! m2	118 sq.ft

• Number of filter elements ................... ll pes

• Suction capacity at 500 mm wg..........560 lis	l 200 cfm

• Suction hose diam............................... l27 mm 	5"

• Cleaning air pressure, max . ...............7.5 bar 	109 psi

• Cleaning air consumption ...................2-4 1/pulse    0.06-0.12 cu.ft/pulse

and drilling.

Electrical system

• Voltage ............................................... 24 V

• Batteries ............................................. 2 x 12 V, 185 Ah

• Alternator............................................ 28 V, 95 Ah

• Work lights, front................................ 6 x 70 W

• Work l ights, rear ................................. 2 x 70 W

• Work lights, feed................................. 2 x 70 W

| Volumes • Hydraulic oil tank .............................. 250 I | 65 | US gal |
| --- | --- | --- |
| • Hydraulic system, total ...................... 300 I | 79 | US gal |
| • Compressor oil............................. .... ... 24 I | 6.3 | US gal |
| • Diesel engine oil ................................. 28 I | 7.4 | US gal |
| • Diesel engine, cooling water .............. 35 I | 9.2 | US gal |
| • Diesel engine, fuel tank ...................... 330 I | 87 | US gal |
| • Traction gear ....................................... 3 I | 0.8 | US gal |
| • Lubrication tank (ECL) ...................... I 0 I | 2.6 | US gal |

• Warning lamp and reverse buzzer

|  | Fle xiROC T35 R | 20 kW | 2 6.8 hp | 230 bar | 3 335 psi | 42-50Hz | 1180 Nm |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | FlexiROC T40 R | 25 kW | 33.5 hp | 230 bar | 3 190 psi | 44Hz |  |

I

Transport dimensions 	FlexiROC T35 Rand  T40 R

Feed dumped 2

Dimensions and weight

| V\{eig_ S ndard unit ex(;luding a!l opti n |  |
| --- | --- |
| FlexiROC T35 Rand T40 R |
| Tier 3 | 1ier4 |
| 1 4 100 kg 1 31 ogo lb | 14 4oo kg 1 31 750 lb |

;_and drill steel-J

X

0

Selection of optional equipment

Carrier

• Hydraulic support  leg

• Hydraulic winch with tow­

ing eye and wire guides, radio remote controlled

• Diesel engine preheater

• Air flow switch

• Electric refuelling pump

• Service hand ligh ts inside canopy, 2 pes

• Combined  warning sound and warning light

• ProCom satellite  based drill rig monitoring  system (only

in combination w ith a written

service agreement)

Feed

• Toe hole drilling kit

• Sleeve retainer for RRS 51

-Jaw set R32/T38

-Jaw set T45/T51

• TAC guide tube guides for drill steel support

- TAC 45 mm for 45 mm guide tube

- TAC 56 mm for 56 mm guide

tube

- TAC 64 mm for 64 mm guide tube

- TAC 76 mm for 76 mm guide tube

Hole measuring systems

• Laser receiver upgrading  kit

• Electronic  inclination  and hole depth instrument

• GPS compass for parallel holes

Lube oil, lu be system  and  water mist system

• Rock drill oil collecting  system

(standard on FlexiROC  T40 R)

• Central lubrication system, type

Lincoln

• Thread greasing devise ECG (with oil)

• Thread greasing device, rush

type (with grease)

• Artie hydraulic oil, VG 32

• Tropical hydraulic oil, VG

68

• Bi ological  h yd raulic oil, VG 46

• Water mist system, 120 Iwater tank

• Water mist system, excluding

tank

Dust  control

• Dust pre-separator (standard on

FlexiROC T40 R)

• Rubber disc for OCT

• Rubber skirt for OCT

Delivered eq uipment, not mounted

• Gas charging equipment  for rock drill

• First 50 hours serv ice kit for

compressor

• Conversion  kit R38/T38 (not for

FlexiROC T40 R)

• Conversion  kit T45

• Conversion  kit T51

• Spare code key for radio trans­

mitter